## Slide 1: Samantha Ramsey Multi-body Dynamics Research Group
Presentation 16
9/14/2023

## Slide 2: Manifold follow up
Does it matter if you normalize the step off from the orbit onto the eigenvector using the only the position elements of the eigenvector vs the entire state?
At first glance – maybe?
But if we add in more manifolds the overall surface they cover looks the same

## Slide 3: Initial conditions for the manifolds
Blue line is the stable eigenvector
Notes: The solution being periodic means that the rates of contraction or expansion along the orbit are the same so we can transition the eigenvectors using the STM at a series of points around the orbit equally spaced in time

## Slide 4: Initial conditions for the manifolds
Blue line is the stable eigenvector
Choice between position and full state only effects the magnitude of the step off onto the eigenvector
Added as an input to the manifold function but have to be extra careful of step off distance
  Using full state to normalize and a smaller step off could lead to more numerical error build up
Notes: The solution being periodic means that the rates of contraction or expansion along the orbit are the same so we can transition the eigenvectors using the STM at a series of points around the orbit equally spaced in time

## Slide 5: Homoclinic Trajectories
Exist where stable and unstable manifolds of an orbit meet tangentially
  Depart the orbit asymptotically on an unstable manifold
  Travel along it and eventually transition onto the stable manifold at a tangential crossing
  Asymptotically re-approach the periodic orbit
Can be identified using Maps
  Select a hyperplane and plot the states of the manifold at the crossing
  Look for places where the stable and unstable manifolds cross
Shown is a map for the first x-axis crossing on the Lunar side for manifolds propagated from an L1 Lypaunov orbit
  Two potential transfer locations
Notes: The solution being periodic means that the rates of contraction or expansion along the orbit are the same so we can transition the eigenvectors using the STM at a series of points around the orbit equally spaced in time

## Slide 6: Targeting: Tau-Alpha
Want: continuity at and , perpendicular
crossing at y=0
Controls: time traveled along PO, , time traveled along manifold

## Slide 7: Targeting: Tau-Alpha
Update matrix is the derivative of the constraints wrt
the free variables
(but actually )
Relate final state to changes in initial state – STM!
Time derivatives
This one was the fun term – derivation in back up slides

## Slide 8: Targeting: Tau-Alpha
Constraints equal to the number of free variables:
  Unique solution! 

## Slide 9: Current Progress
Segment 1 integrated from to on periodic orbit
Segment 2 integrated from to along manifold
Notes: The solution being periodic means that the rates of contraction or expansion along the orbit are the same so we can transition the eigenvectors using the STM at a series of points around the orbit equally spaced in time

## Slide 10: Moving forward
Some suspicious eigenvalues in stored data for previously computed orbit families
  Recompute to check these + store additional information
L1 Lyapunov orbit Homoclinic connection
  Maps
  Tau-Alpha
L1 to L2 Lyapunov Heteroclinic connection
  Fixed JC targeter

## Slide 11: Non-Research
Class
  AAE 590 (Spaceflight Operations)
Literature review
  Improve methods for finding relevant technical papers, close reading, and organization
Continue exploration of the problem space
  Manifolds from wide range of orbit families
  Stability investigation
  Stretching directions
    Stable vs unstable orbits
Tool development along the way
  Multi-processing/GPU processing
  Multiple shooting
  Tau-alpha
ATD
  Learn to use and validate results
  Look into Java under the hood to learn how to write software for exploration
Bi-circular restricted 4 body model
Research Goals
Personal
Work more efficiently
  And hopefully less
Go to at least 2 group outings